## Slide 1: Turbidity Meter Simulation
Pre-Results Meeting

## Slide 2: The Experimental Setup
The source
Domain Boundary
Zone(1) of interest
Zone(2) of interest
3D image of the experimental setup
X-Z plane of the experimental setup
The setup(1) consists of a source in the middle of out domain. The domain boundary is absorbant, and the source is a pencil source.

## Slide 3: Simulation Innerworkings
Photon launches with a packet weight 1 and direction v
Based on an exponential distribution based on the scattering coefficient (μs) of the current voxel, it decides how many voxels to travel in v direction.
Steps 1 voxel in v direction and looses packet weight based on the absorption coefficient (μa)
The packet weight is added to its current voxel’s raw probability,
The previous 2 steps are repeated until the package reaches the next scattering voxel decided in the second step
Calculate a new scattering direction vector: the azimuth and zenith scattering angles are computed, respectively, by a random number uniformly distributed in [0,2pi] and a random number between [0,pi) following an assigned phase function.
Repeat from step 2 until the max time is reached or the photon exits the domain
Repeat all steps for next photon

## Slide 4
Photon Launches with weight 1 in v dir
Based on μs, photon travels n voxels
n
Weight is reduced based on μa
New scatter direction is determined
Previous steps are repeated until the boundary is left or no more time is left

## Slide 5: Monte Carlo Simulation Result

## Slide 7: Angle test
For smaller radius the difference between the peak and bottom plateu become smaller from 4 times to 3 times the difference.
The issue is that these voxels have no min acceptance angle, so this is not an accurate representation of what the detector would see.

## Slide 8: A better way
Imagine the image below is the x-y slice where the source is. The idea is to measure the light exiting the top boundary. Represent the intensity at the boundary along the y direction in a bar graph. Hence we know the best position to place the detector. The same can be done at the front face.
X-dir
Y-dir
50mm

## Slide 9: Results for the off beam detector at 50 mm

## Slide 10: Results for the off beam detector at 50 mm continued

## Slide 11: Results on the face perpendicular to the beamline at 100mm

## Slide 12: What if we go higher off the beam?
AT 100mm off beam
AT 50mm off beam

## Slide 13: Sanity Checks
Under 0 scattering:
  Peak at zero degrees
  Absorption dependance must recover the beer lambert law
Under conditions where 1 scattering event per photon on average occurs:
  We must recover the Fornier Forand distribution
  HG and FF must be close
Under reasonable scattering:
  Increasing photon number must reduce std of solutions
  HG and FF must divarge
Under very large scattering:
  Source must look isotropic at a distance with no forward bias
  HG and FF must converge

## Slide 14: Zero Scattering Check
X-Y Slice of Monte Carlo Sim
Fluence measured at angles

## Slide 15: Absorption/Beer-Lambert Crosscheck
Absorption Coeff | Normalized Fluence | Beer-Lambert
1e-7 | 1.000 | 1.000
1e-5 | 1.007 | 0.999
1e-4 | 0.990 | 0.990
1e-3 | 0.904 | 0.904
1e-2 | 0.366 | 0.367
0.1 | 4.32e-5 | 4.54e-5
0.5 | ~0 | ~0

## Slide 17
250mm
250mm
250mm
Source

## Slide 18
Variable lenght
30mm
100mm
Each square serves as a detector

## Slide 21
Beam Line Detector
Off the Beam Line Detector
Light Source

## Slide 22
Beam Line Detector
Off the Beam Line Detector
Light Source
15mm
75.5mm

## Slide 23
75mm

## Slide 24
75.5mm

## Slide 25
Source
Measurement at distance
Measurement at distance